## Slide 1: Multichannel high speed camera with 10 GbE interface
Master Thesis
Supervisor: PhD Grzegorz Kasprowicz
Author: Piotr Zdunek
Photonics and Web Engineering Group, Institute of Electronic Systems, Warsaw University of Technology

## Slide 2: Agenda
Introduction
System overview
  Multichannel operation
  Zynq SoC
  Data acquisition
  10 GbE
Project’s schedule

## Slide 3: Introduction
There is a need for a multiple sensor camera – in a form of a strip
Real time operation
Scalable
Easy to maintain
Supporting high speed interfaces (10 GbE)

## Slide 4: System overview

## Slide 5: System overview

## Slide 6: Xilinx Zynq
2x Cortex A9
  Lots of peripherials
Kintex FPGA
High throughput interconnect

## Slide 7: Multichannel operation
External or internal clock signal
External trigger
Synchronised frame acquisition with timestamp (IEEE1588)

## Slide 8: Data acquisition
CMV4000 generates 4MP of data per frame over 16 LVDS lines
Maximum 180 fps
Maximum sensor clock is 480 MHz
180*4MP*10bit = 7200 Mbps

## Slide 9: 10 GbE UDP IP
Stream data through Ethernet using UDP
Get rid of PHY – use GTX
  Cheaper solution
Create custom GbE UDP IP
  Which would incorporate hardware MAC in Zynq
EMIO – Extended Multiplexed Input Output

## Slide 10: Project’s schedule
Learn how to use Zynq and Vivado/PlanAhead
Sensor driver (IP Core) in programmable logic – end of June
Sensor control in Cortex A9 using FreeRTOS – end of July
Sensor data streaming through built in Ethernet MAC – end of September
Multichannel data acquisition synchronisation – end of October
Develop 10 GbE UDP IP core – end of year
Tests – till Feburary

## Slide 11: Thank you for your attention
Piotr Zdunek